JARAMOGI OGINGA ODINGA UNIVERSITY OF SCIENCE AND TECHNOLOGY

SCHOOL OF ENGINEERING AND TECHNOLOGY

UNIVERSITY EXAMINATIONS    FOR THE DIPLOMA IN BUILDING AND CIVIL ENGINEERING

2ND YEAR 2ND SEMESTER 2017/2018 ACADEMIC YEAR

CENTRE: MAIN CAMPUS

---------------------------------------------------------------------------------------------------------

COURSE CODE: TBC 2223

COURSE TITLE:    HYDRAULICS II

EXAM VENUE:   LAB 23                            STREAM: DIP IN BLD & CIV ENG

DATE:  20/12/2017                         		 EXAM SESSION: 9.00 – 10.30AM

DURATION: 2 HOURS

--------------------------------------------------------------------------------------------------------

Instructions

- Answer question 1 (Compulsory) and ANY other two questions

- Candidates are advised not to write on question paper

- Candidates must hand in their answer booklets to the invigilator while in the examination room

QUESTION ONE (30 MARKS)

- State and outline the significance of the following;				(6 Marks)

- Continuity equation

- Bernoulli’s Equation

- Explain what you understand by an open channel flow and distinguish between uniform and non-uniform open channel flow.							(8 Marks)

- Outline the difference between turbulent flow and laminar flow; hence explain how Reynolds’s number is used to determine the different types of flows.		(6 Marks)

- Explain the principle involved in measuring velocity of flow using a pitot static tube.

Hence determine the velocity of air, if a pitot static tube is used to measure the velocity of air flowing through a duct, and the manometer shows a difference in head of 5 cm of water. The density of air and water are 1.13 kg/m3 and 1000 kg/m3. Assume the coefficient of the pitot tube as 0.98.

(10 Marks)

QUESTION TWO (15 MARKS)

- A venturimeter of 150 mm × 75 mm size is used to measure the flow rate of oil having specific gravity of 0.9. The reading shown by the U tube manometer connected to the venturimeter is 150 mm of mercury column. Calculate the coefficient of discharge for the venturimeter if the flow rate is 1.7 m3/min. (Note: The size of venturimeter generally specified in terms of inlet and throat diameters).				(10 Marks)

- Briefly explain what you understand by the term, “Economical cross-section” with reference to an open channel. 							(5 Marks)

QUESTION THREE (15 MARKS)

- Explain what is meant by energy losses in a pipe, distinguishing both the major and minor losses.    									(7 Marks)

- Show that the loss of head due to friction, hf, is given by;

; where f is the resistance coefficient, L length of the pipe, v is the mean velocity of flow, d is the pipe diameter and g the gravitational acceleration.											(8 Marks)

QUESTION FOUR (15 MARKS)

- Define venacontracta, and derive the expression for flow measurement through an orifice in an open tank.										(9 Marks)

- State Chezy and Manning formula for uniform flow through an open channel. (6 Marks)

QUESTION FIVE (15 MARKS)

- Derive an expression for the flow measurement using a triangular notch in an open channel.(9 Marks)

- Discuss the method of velocity measurement using (i) Vane anemometer and (ii) Turbine meter. 									                   (6 Marks)