JARAMOGI OGINGA ODINGA UNIVERSITY OF SCIENCE AND TECHNOLOGY

SCHOOL OF ENGINEERING AND TECHNOLOGY

UNIVERSITY EXAMINATIONS    FOR THE DIPLOMA IN BUILDING AND CIVIL ENGINEERING

3RD YEAR 2ND SEMESTER 2017/2018 ACADEMIC YEAR

CENTRE: MAIN CAMPUS

---------------------------------------------------------------------------------------------------------

COURSE CODE: TBC 2322

COURSE TITLE:    CIVIL ENGINEERING CONSTRUCTION II

EXAM VENUE:  LAB 23                             STREAM: DIP IN BLD & CIV ENG

DATE:  11/12/2017                         	          EXAM SESSION: 9.00 – 10.30 AM

DURATION: 1 ½  HOURS

--------------------------------------------------------------------------------------------------------

Instructions

- Answer question 1 (Compulsory) and ANY other two questions

- Candidates are advised not to write on question paper

- Candidates must hand in their answer booklets to the invigilator while in the examination room

QUESTION ONE (COMPLULSORY) (30 MARKS)

- With the aid of neat sketches, explain any four types of retaining walls  (12 Marks)

- Explain three dewatering techniques employed in basement construction (3 marks)

- State some of the advantages and disadvantages of using Tunnel Boring Machines (TBM) in tunneling

(6 Marks)

- Determine the total horizontal force acting on a 5m high retaining wall supporting a backfill of internal angle of friction of 30o and a unit weight of 20kn/m3. There is a surcharge of 25KN/m2 on the backfill material ( 6 marks)

- Explain any three advantages of reinforced concrete water tanks over plastic water storage tanks. ( 3 marks)

QUESTION TWO (15 Marks)

- Explain any three ways, giving examples, how tunnels can be classified in civil engineering. ( 3 marks)

- Explain the two main purposes of permanent tunnel linings (4 Marks)

- Describe any four types of materials used for lining bored tunnels. (8 marks)

QUESTION THREE (15 Marks)

- Using neat sketches, describe the following types of concrete dams.  (9 Marks)

- Gravity Dams

- Arch Dams

- Buttress Dams

- State some of the advantages and disadvantages of concrete dams ( 6 marks)

QUESTION FOUR (15 Marks)

With the aid of neat sketches, where necessary explain the following methods of ground water control in basement construction. (15 Marks)

- Sheet Piles

- Diaphragm walls

- Grouting

QUESTION FIVE (15 Marks)

a) Explain any two scenarios where pile foundations would be more ideal (2 mark)

b) Differentiate between Displacement and Replacement piles (4 marks)

c) The cantilever wall shown blow is backfilled with material having a unit weight of 19kn/m3 and internal angle of friction of 30o. Calculate the factors of safety against sliding and overturning. Assume the coefficient of friction as 0.4 and unit weight of concrete as 24kn/m3. (9 marks)